## Slide 1: Mobile Display Measurement System User Guide (Android)
Host System Example: Windows 7 64-bits with Matlab R2012a
Mobile Device Example: Samsung Galaxy S3 (Android 4.1.1)
12/10/2012

## Slide 2: System Requirement
Mobile
Display
CS2000
Host System
Ethernet Router
Wifi Hub/Switch
TCP/IP Pattern Stream Program (Matlab)
APK
CS2000 Measurement
Control Program (Matlab)
Pattern Stream
Test Pattern Folder
Mobile Display Measurement System
Instrument Requirement List
Host System (Including Matlab)
Ethernet Router
Wifi Hub/Switch
KONICA MINOLTA CS2000

## Slide 3: Mobile Device Software Installation
1. Connect Mobile system to the host system
2. Find mobile device Item, and Click it.

## Slide 4: Mobile Device Software Installation (cont’)
3. Copy the control program “RemotFB.apk”into “GT-I9300/Phone/Download/” folder
4. Disconnect Mobile and host System

## Slide 5: Mobile Device Software Installation (cont’)
5. Click My Files, and into the “Download/” folder

## Slide 6: Mobile Device Software Installation (cont’)
6. Click “RemoteFB.apk”
6.a* If you see this dialog box, Please click “Settings” bottom
6.b Please select “Unknown Sources”
6.c Please click ok to accept install unknown sources
* If you don’t see any information about install blocked, please skip this page.

## Slide 7: Mobile Device Software Installation (cont’)
7. Click the “Install”
8. If install successfully, you will see the App “RemoteFB”

## Slide 8: Mobile System Measurement Setup
1. Find Setting App, and Click it
2. Find Display Item, and Click it.

## Slide 9: Mobile System Measurement Setting (cont’)
3. Please set Screen timeout to 10 mins.
4. Brightness set to 25, 50, 75, or 100%.
25%
50%
75%
100%
0%

## Slide 10: Mobile System Measurement Setting (cont’)
5. Connect KNOICA MINOLTA CS-2000 and target mobile device to the host system, prepare to measurement.

## Slide 11: Host System Software Installation
1. Put all test patterns in the same folder
2. Please run the measurement program of “rs232_cs2000a_mobile.m”

## Slide 12: Host System Software Installation (cont’)
3. Find out the IP address of your android phone in settings->wireless & networks->WiFi settings->”Your WiFi network name”
4. In MATLAB, call the function boxSendImg(file, host, port, number_of_retries), in which file is the path of a image file, host is the IP address of your android phone, port is 8080

## Slide 13: Host System Software Installation (cont’)
5. After you run the program, you will see this dialog box.
6. Select your test pattern folder, and press “ok”

## Slide 14: Host System Software Installation (cont’)
7. Select your record file name, and press enter to start the measurement